Title: SD Card Print Interruption
Test Plan: TP-RD-00002
Document Date: 01.28.16
Test Date: 01.26.16
Testing Location: Aleph Objects Inc., Loveland, CO

PURPOSE:
Discover the cause of prints from SD stopping.

RESULTS SUMMARY:
The root cause is due to a bad memory cell in the NAND flash memory of the SD card.

CONCLUSION:
When the address with the damaged floating-gate transistor is accessed through the RepRap Discount Smart Controller the SPI serial clock experiences a ripple on the slave end (RRDSC) which causes the master and slave to lose synchronization which is not recovered.

BACKGROUND INFORMATION:
The SPI bus has the following four communication lines:
- SCK – Serial clock (used for synchronization between the master and slave)
- MOSI – Master-out slave-in (requesting an address or writing data to the SD card)
- MISO – Master-in slave-out (reading data from the SD card)
- SS – Slave select (acknowledging the presence of an SD card)

If synchronization is lost then the master and slave are no longer able to communicate properly.

EQUIPMENT:
Nutwort 04 and additional TAZ 6 prototype unit.

PROCEDURE:
Use the G-code M26 S###, where ### represents a given byte on the file, to skip to just before where the malfunction occurred. If the print stops at the same location using the same file on the same SD card and it is repeatable then a defect on the die can be assumed. Repeat the same procedure on the same SD card this time using a copy of the file in the memory, if the print does not stop in the same location then the assumption is verified.

TEST DATA and COMPLETE RESULTS:
The error was found to repeatably occur on byte 21200896/55428356 of the file. The test was performed on two distinct machines and occurred repeatably at the exact same location in the file.

OTHER INFO:
Transmission line theory says that if the length of the communication line is %> %lambda over 10 where λ refers to the wavelength of the propagating signal then it must be treated with transmission line analysis. In our case the wavelength would be:
%tau_rise ≅ 2ns newline %lambda = 0.75 cdot c cdot (2ns) = 0.7(3times10^8 m/s)(6times10^{"-"9}s)=45cm
Since the length of our SPI cable is 18 cm (plus ~5cm from the track) impedance mismatching/signal reflections are not as much of a concern as they could potentially be.

A factor which may assist with such issues is through the use of SD cards which are designed with the use of Single Level Cell (SLC) NAND flash memory. Many cheap NAND flash memory devices make use of memory a technology known as Multi Level Cell (MLC) NAND flash. In MLC four or more bits can be stored in a single floating-gate transistor, introducing a wider (worse) noise-margin and the potential of having corrupt data stored. SLC only stores a single bit per floating-gate transistor allowing for a much narrower (better) noise-margin. These may help shed some light:
https://en.wikipedia.org/wiki/Multi-level_cell
http://panasonic.net/avc/sdcard/industrial_sd/lineup.html#teci

Here are block diagrams of the SPI implementation in the Atmega2560:

Atmel ATmega2560 datasheet