AO-100 &101 Overhaul/Refurbishing Check List
Unplug stepper motors from board before starting to prevent frying the Tosduino's voltage controller

Axises
__Clean/Replace X-axis bushings
__Clean X-axis rods
__Clean/Replace Y-axis bushings
__Clean Y-Axis rods
__Check Z Couplers
__Z-wobble/Nut slop
__Clean Z-axis Rods
__Lighlty lube/clean Z-screws 1-3 drops of oil
__Check Belt tension
__Check for missing teeth on belts
__Check set screw on pulleys
__Check for belt alignment, they should not be rubbing on the sides and should be near the middle of bearings
__Check Motor Tuning

Budaschnozzle
__Check/Replace melted buda plate
__Check/Replace charred lower wood plate on buda
__Check for buda wiring short
__Check buda thermistor resistance should be around 100K ohms at room temp
__Check buda resistor resistance should be between 5.0 to 6.0 ohms
__Check crimps on buda wiring, Should be really crimped and insulated with small tubing
__Check for low temp (semi-clear) PTFE tubing in Buda, if found replace with high temp PTFE tubing (solid white)
__Check for blowout between buda and heatsink and clean if found.
__Check/Clean Nozzle with small wire brush
__Check visual to see if nozzle hole is clear and circular

Extuder
__Check extruder motor, no shorts in coils or wires, no bad internal bearings
__Check/Replace extruder bearings if seized
__Check/Replace extuder idler bearing if seized
__Check to see if Hob bolt is straight and not bent
__Clean Hob bolt teeth
__Check for worn gears
__Check gear spacing should just be touching but not forced together
__Check set screw on small gear.
__Check nut on hob bot is tight enough so bolt does not wiggle but still should spin easily
__Check/Replace wire harness if not 4 pin connector for budaschnozzle

Final Steps
__Clean Heat Bed (red plate)
__Bed level
__Check Skew X_Y_ and Z_
__Check extruder calibration
__Table twist, should not hit the sides when traveling in Y
__Labels on front and back of printer for fleet position
__Label for secondary serial number
__Clean/Remove bubbles or if needed Replace PET sheet.
__Check endstop positions and clearances
__Check for loose USB connection.