Printing Process
- Install Cura 2 from http://devel.lulzbot.com/software/Cura2/
- Once installed, select proper printer
- Begin with your profiles that are already included within Cura 2
  - To do this go to Settings > Profile > (select profile) > Duplicate > New Name
  - Press the Activate button to enable the new profile
  - Once you have the profile to the settings as you like, go to:
    - Settings > Profiles > Manage Profiles > Custom Profile > (Select Profile) > Update profile with current settings
    - Now select Export to save changes as a .curaprofile
- As a note, USB printing has not yet been enabled. In order to print your gcode file, go to Save to File in the lower right hand corner.
  - You can then load the gcode onto the SD card for TAZ 6 printing
  - For Mini Printing you will need to load the Gcode file into our older version of Cura (lulzbot.com/cura)

Submitting Updated Profiles/New Profiles
- Sign up for our code repository at code.alephobjects.com
  - Once signed up, you can submit your updated profile here: https://code.alephobjects.com/project/board/10/ under the profiles column
  - Any other issues or problems you notice, please open a task as well
- When submitting a profile be sure to include:
  - .curaprofile you exported above
  - Which version of Cura 2 you used to generate the profile

Reviewing Submitted Profiles
- We will evaluate profiles based upon cosmetic standards
  - The three profiles we would like is a Standard, Fast, and High Quality
    - Standard = 0.25mm layer height
    - Fast = 0.32mm – 0.4mm layer height
    - High Quality = 0.12mm – 0.18mm
  - We recommend starting with the Standard profile, as changes needed there are usually required for the other two as well.
  - The STL files we will use for evaluation can be found here: http://devel.lulzbot.com/filament/Testing_Docs_Master/