Z Lower left/right (2)
  - 8mm fit
  - good to print

Z Upper left/right (2)
  - 8mm fit
  - good to print

X end Motor (1)
  - Wire routing around back
  - 8mm fit
  - Holes for Zip tie – top as close to flange as possible and bottom 20-25mm lower. 3Mm holes min
  - Z min switch mount – body 1mm below

X end Idler (1)
  - 8mm fit
  - Make insert counterbore shallower
  - good to print

Y rod mount (1)
  - Adjust for 315mm rods
  - 8mm fit
  - good to print

Y Idler mount (1)
  - 8mm fit
  - good to print

Belt mount (2)
  - change to clamp design
  - insert direction
  - add teeth to insert side
  - add step to bolt side
  - lower screw by 2mm
  - Lower face by 1mm
  - cut belt exit back
  - make teeth grooves shallower
  - make grove narrower

Bearing holders (4)
  - Use less material
  - Lower X simple
  - Upper X add flange for cable guide

Bed cover (1) (Brent)
  - add exhaust cutout
  - lower for new washer
  - add lowering tab by fan cutout

Bed corner (4) (Brent find file)
  - good to print

Spool Hinge/Arm/mount (3)
  - Adjust for fit around case
  - remove taper
  - Make cleaner if possible
  - Make wider
  - cot out other side
  - taller

Strain relief/clamp (2)
  - incorporate Cable guide mount
  - make wire list to pass thru
  - clamp

LED mounts (2)
  - front right corner
  - see what fits in front left

Freedom Sandwich case (3)
  - SD card access
  - Space over LED plug = 20mm
  - print concept, wait for final base/core/LDC
  - Angle adjustment bracket

X-Carriage (1)
  - Stronger
  - stop blower from spinning
  - good to print

Extrusion Fan (1)
  - good to print

Extruder Body (1) (Brent)
  - Deeper hole for Hex nozzle
  - remove filament out hole and step

Large gear (1)
  - good to print

Small gear (1)
  - good to print

Washer (1)
  - good to print

Idler (1)
  - good to print

Finger latch (1)
  - good to print

Bed fan mount (1)
  - good to print

Handle (1) (Brent)
  - new design being tested