FAILURE ANALYSIS REPORT

NAME: Brent MacKenzie	DATE: 10/27/2014
ITEM DESCRIPTION: / Heater cartridge for AO-Hex hotend	SERIAL NO: / N/A
FAILURE REPORT DATE: 10/15/2014	ORIGIN: Internal / R&D

FAILURE MODE/ DESCRIPTION: / 2 Lulzbot mini prototypes with the AO-Hexagon hotend have shown heater failure, with the hotend simply failing to heat when a temperature is set.	SYMPTOMS: / Hotend not heating up or heating up very slowly / Thermistor resistance is ~100 kOhm at room temp (normal) / Heater resistance is >>6 Ohm (~1 Mohm) / No visible damage to the heater cartridge

OBSERVATIONS & FINDINGS & PICTURES / There was no visible damage to the resistor or thermistor / The Firmware had the PID set to cut the 24V supplied power to 12V, the cartridges rated voltage / Multimeter probing of the heater terminals revealed voltage spikes up to 18V from the firmware PID control / The PID settings were altered in the firmware to keep peak voltage below 12V to protect the heaters from damage.

CONCLUSION/ ROOT CAUSE: The firmware PID controls were allowing higher than 12V peaks in the PID control, exceeding the heater's rating. No failures have been observed with the new firmware patch.

CORRECTIVE ACTIONS/ FIXES	OWNER	COMPLETION DATE
Update firmware on all in house testing machines	Brent M.	Done
Get firmware updates to the 2 begonia printers, as well as new heater cartridges if necessary	Brent M.	11/29