AO-Hex Hotend-Subassembly – LulzBot Mini

Required Tools: Torque wrench with 7mm crows foot adaptor, 18mm open end wrench, 4.5mm open end wrench, 1.5mm hex screwdriver, 2mm hex screwdriver, high temperature thread-locking compound

Unscrew heatsink and nozzle – reinstall nozzle using a 7mm torque wrench and holding the heater block with a 18mm wrench. Tighten to 30 in*lbs. Make sure that the nozzle says 5 on the side (0.50mm nozzle).

- Apply thin coat of high temperature threadlock to the entire threaded portion and re-install in the heater block. Install tightly using a 4.5mm wrench and holding the heater block with a 18mm wrench
  - If possible, rotate the heatsink so that one of the points of the heatsink faces the front and the set screw hole is somewhere in the back.
- Lock the threaded extension into the heatsink using an M2x6 SCHS with a small amount of high temperature thread lock.
- Cut thermistor and heater cartridge wires to 180mm and crimp on male pins
- Take thermistor and pull back both pieces of the black shielding 1/2”
  - Make sure that the inner clear plastic tubing is all the way down to the bead of the thermistor

Slide ONE of the pieces of black shielding down to the bead of the thermistor and insert into the heater block

- Holding the thermistor leads in place, install the heater cartridge, but do not lock in place yet
- Secure heater cartridge and thermistor into the side of the heat block with a retention plate and an M3x6 BHCS.
  - Be sure that the retention plate is tightened seated completely flush against the block
  - Make sure that the front edge of the plate is parallel to the front face of the heater block.
  - Make sure that the retention plate is covering part of the heater cartridge
  - Make sure that both leads of the thermistor are in the channel in the side of the heater block and not pinched against the flat face. One of the 2 black shield bits should be secured by the retention plate, the other should rest flush with the top of it.

- Pull heater cartridge up against the retention plate and lock into place with am M3x6 set screw from the rear of the heater cartridge.
- Attach ground lug to the left side of the heater block using an M3x6 BHCS and star lock washer between the ground lug and the heater block.
  - make sure that the wire is facing toward the heatsink so it can be routed with the other leads